### ✅ 1. Disable Wi-Fi and Access Point
You’ve already done this — good!
import network

wlan = network.WLAN(network.STA_IF)
wlan.active(False)

ap = network.WLAN(network.AP_IF)
ap.active(False)
### 🌙 2. Use machine.lightsleep() or machine.deepsleep()
- These reduce CPU activity.
- Lightsleep retains RAM and most state.
- Deepsleep consumes even less, but resets the Pico on wake.
import machine

machine.lightsleep(1000) # sleep for 1000 ms
### 💤 3. Lower the CPU frequency
You can reduce the CPU clock from the default 125 MHz to, say, 48 MHz:
import machine

machine.freq(48_000_000) # set to 48 MHz
### 🔌 4. Turn off unused peripherals
If you're not using:
- I2C
- SPI
- ADC
- PWM
  you can de-initialise them:
i2c = machine.I2C(0)
i2c.deinit()
### 🟢 5. Avoid floating GPIO pins
Set unused GPIOs to Pin.IN with Pin.PULL_DOWN or PULL_UP to prevent leakage:
from machine import Pin

for i in range(2, 29): # GPIO 2–28
    Pin(i, Pin.IN, Pin.PULL_DOWN)